## Slide 1
Edited and presented by :
Marwa Al-Hadi
Lecture 4: Data collection (sensor)

## Slide 2: Identify your problem
2
What is your problem?

## Slide 3: Data Science
3
Ex:IoT

## Slide 4: Types of Data Sources
Primary Data:
  Data collected directly from the source.
  Examples: Surveys, experiments, IoT sensors.
4

## Slide 5: Introduction to IoT and Data Science
Internet of Things (IoT) refers to interconnected devices that collect, transmit, and process data through the internet.
5

## Slide 6: Introduction to IoT and Data Science
Internet of Things (IoT) refers to the network of physical devices connected to the internet, enabling them to collect and exchange data.
6

## Slide 7: Introduction to IoT and Data Science
Examples:
  wearable devices (e.g., fitness trackers),
  and industrial sensors.
7

## Slide 8: Introduction to IoT and Data Science
IoT in Data Science
  IoT generates vast amounts of real-time data.
  These datasets can be used for predictive modeling, analytics, and decision-making in areas like healthcare, agriculture, and smart cities.
8

## Slide 9: Steps in IoT Data Collection
1. Identify the Purpose
Define the problem or objective for collecting IoT data.
Examples:
  Monitor heart rate using wearable devices.
  Measure soil moisture levels for precision agriculture.
  Track energy consumption in smart homes.
9

## Slide 10: Steps in IoT Data Collection
2. Choose IoT Devices
Select devices based on the data required:
  Sensors: Measure physical parameters (e.g., temperature, humidity, light, motion).
  Actuators or Arduino ..etc.: Respond to data by taking actions (e.g., turning on a fan).
  Wires or wireless or Bluetooth for connection
10

## Slide 11: Arduino
Basically Arduino is Microcontroller.
Microcontroller is microprocessor with memory, RAM and some other peripheral connected with it.
The Arduino Uno is a microcontroller board based on the ATmega328 . The ATmega328 has Flash memory of 32 KB. It also has 2 KB of SRAM and 1 KB of EEPROM
Notes: Flash- Where program is stored.
SRAM-Static Random Access Memory ( sketch creates and manipulates variables when it runs )
EEPROM- Electrically Erasable Programmable Read-Only Memory ( memory whose values are kept when the board is turned off )

## Slide 12: Arduino
**Flash- Where program is stored.
**SRAM-Static Random Access Memory ( sketch creates and manipulates variables when it runs )
**EEPROM- Electrically Erasable Programmable Read-Only Memory ( memory whose values are kept when the board is turned off )
Notes: Flash- Where program is stored.
SRAM-Static Random Access Memory ( sketch creates and manipulates variables when it runs )
EEPROM- Electrically Erasable Programmable Read-Only Memory ( memory whose values are kept when the board is turned off )

## Slide 13: Different types of Arduino
Arduino Mega 2560
Arduino LilyPad
Arduino Uno
DIY Arduino
Boarduino Kit

## Slide 14: Arduino uno
What does it have?
  14 Digital In/Out pins
  6 Analog Inputs
  A USB Connection
  A Power Jack
  Reset Button
  On-board LED
  SCL/SDA pins (Serial Clock/ Serial Data pins)

## Slide 15: Arduino uno
What does it have?
  In short, it contains everything needed to support the microcontroller; simply connect it to a computer with a USB cable or power it with a AC-to-DC adapter or battery to get started.

## Slide 16
Digital I\O
PWM(3, 5, 6, 9, 10, 11)
SCL\SDA
(I2C Bus)
RESET
PWR IN
USB
(to Computer)
Analog INPUTS
POWER
5V / 3.3V / GND

## Slide 17: How to code in arduino
You need to download Arduino IDE (Integrated Development Environment).
Arduino IDE is available for all Mac, Windows.and Linux.

## Slide 18: How to code in arduino
Once you have downloaded and installed/extracted the folder, you can directly run Arduino.exe, which will take you to its IDE.
The IDE will look like the shown screenshot.
error & status messages

## Slide 19: Program your arduino
Before you start programming, double check that correct board is selected under Tools  Board.
Now, you can start playing with Arduino.

## Slide 20: Program your arduino
The Arduino Uno can be programmed with the Arduino software. Select "Arduino Uno from the Tools > Board menu (according to the microcontroller on your board).
All the peripheral connected with Computers are using Serial Port.
You can check port for Arduino Uno in Device Manger.

## Slide 21: Input vs output

## Slide 22: 6 Major concepts
digitalWrite()
analogWrite()
digitalRead()
If (statements) / Boolean
analogRead
Serial Communication

## Slide 23: Analog vs digital
Microcontrollers are digital devices – ON or OFF. Also called – discrete.
Analog signals are anything that can be a full range of values.
5 V
0 V
5 V
0 V

## Slide 24: Steps in IoT Data Collection
3. Set Up Connectivity
IoT devices use protocols to communicate data:
  Wires: connect using set of wires.
  Wi-Fi: Common for home devices.
  Bluetooth: Short-range communication.
  LoRaWAN: Long-range, low-power communication for industrial applications.
24

## Slide 25: Steps in IoT Data Collection
4. Data Acquisition
Collect data from IoT sensors in real-time.
Use wires, APIs, MQTT, or HTTP protocols to transfer data to a storage system.
25

## Slide 26: Steps in IoT Data Collection.. Using wires
26

## Slide 27: Steps in IoT Data Collection.. Using MQTT
27
Using MQTT (Message Queuing Telemetry Transport):
MQTT is
  a lightweight messaging protocol designed for IoT applications,
enabling devices to send data to a broker that routes it to subscribers.

## Slide 28: Steps in IoT Data Collection ...Using MQTT
28
How It Works:
  Devices publish data to MQTT broker under specific topics (e.g., sensor/temperature(
  Subscribers: receive the data and store it e.g., a database application

## Slide 29: Steps in IoT Data Collection.. Using MQTT
29
Key Components:
  Publisher: The device sending data.
  Broker: that manages message distribution.
    Example : self-hosted or cloud-based, e.g., HiveMQ, AWS IoT
  Subscriber: The system receiving and processing the data..

## Slide 30: Steps in IoT Data Collection.. Using MQTT
30
Example :
  A soil monitor sends data to an MQTT broker.
  A storage service subscribes data and logs the readings in a database.

## Slide 31: Steps in IoT Data Collection.. Using APIs
Using APIs
1. Understand the Use Case:
  Collecting data from a public API.
  Sending sensor data to a cloud API for real-time monitoring.
  Fetching device configurations or updates from a remote server.
31

## Slide 32: Steps in IoT Data Collection.. Using APIs
1. Understand the Use Case:
2. Basic Steps for Data Collection.
  Setup IoT Devices Use IoT hardware (e.g., Raspberry Pi, ESP8266, ESP32, Arduino) equipped with Wi-Fi or other communication capabilities.
  Program the device to interact with APIs.
  Use Appropriate Communication Protocol HTTP/HTTPS for communication.
  Configure API Access: request methods (GET, POST, etc.), and response formats (JSON, XML).
32

## Slide 33: Example of soil moisture sensor
33
our soil moisture sensor: when we stick it in the soil, it checks how much water's in there. The probe has these two metal bits that measure how easily electricity can flow through the soil. More water means easier flow, less water means it's a bit tougher. The sensor then tells us what's up with the soil moisture. It's like having a little meter to check if your plants need a drink!

## Slide 34: Example of soil moisture sensor
34

## Slide 35: Example of Soil Moisture Sensor with Arduino
35

## Slide 36: Example of soil moisture sensor
Components and supplies
Arduino UNO R3 - Made in italy
Breadboard - 830 contacts
Capacitive Soil Moisture Sensor
36

## Slide 37: Example of soil moisture sensor
37

## Slide 38
Compile
Upload
Status Message

## Slide 39: Code Arduino soil moisture sensor code
// Moisture Sensor Arduino Code
//By Circuitdigest
#define ledPin 6
#define sensorPin A0
void setup() {
Serial.begin(9600);
pinMode(ledPin, OUTPUT);
digitalWrite(ledPin, LOW);
}
void loop() {
Serial.print("Analog output: ");
Serial.println(readSensor());
delay(500);
}
// This function returns the analog data to calling function
int readSensor() {
int sensorValue = analogRead(sensorPin); // Read the analog value from sensor
int outputValue = map(sensorValue, 0, 1023, 255, 0); // map the 10-bit data to 8-bit data
analogWrite(ledPin, outputValue); // generate PWM signal
return outputValue; // Return analog moisture value
}
39